## Slide 1: LTE Air-to-Ground Test Case 2
Assessment, Conclusions, Recommendations & Executive Summary
ESN Mynydd Rhiw Wide Beam Antenna Campaign

## Slide 2: Test Objectives
Evaluate airborne LTE coverage using Bands 3, 20 and 40
Assess wide-beam antenna performance at 1,500 / 3,000 / 6,500 / 10,000 ft
Assess VoLTE continuity, mobility and RF stability
Investigate airborne coverage over sea and sector-edge behaviour

## Slide 3: Key Network & Test Conditions
Band 40 intended as primary airborne layer
Bands 3/20 provide opportunistic terrestrial backfill
Wide-beam 260° sector with known overlap limitations
Active test setup introduced approximately 12 dB insertion loss
Sea-reflection and multipath environment creates challenging RF geometry

## Slide 4: Overall RF Findings
Band 40 dominates at medium/high altitude
Coverage quality degrades with distance (especially beyond 30–50 km)
Sector-edge degradation consistently observed
Left-hand/anticlockwise wide-beam edge is weakest region
RSRQ/SINR instability driven by geometry and multipath rather than power alone

## Slide 5: Operational Findings
VoLTE performance substantially worse than RF metrics alone suggest
Call setup failures and poor MOS concentrated at WB antenna sector edges and outer arcs
Best operational performance achieved within beam centre of the WB at 10–30 km
Performance becomes unreliable at 50–70 km
Bands 3/20 assist near land but cannot reliably support airborne service above 500 ft

## Slide 6: Impact of 12 dB Test Loss
12 dB loss significantly degraded measured RSRP, SINR and MOS
Measured performance represents conservative/worst-case behaviour
Removing 12 dB loss would likely improve call setup success MOS and UL stability
However, geometry-driven issues would still remain
Poor SINR/RSRQ regions and mobility instability are not purely power-limited

## Slide 7: Serial 2.1 – 10,000 ft
Band 40 dominant across orbit
Persistent degradation between 130°–220° wide-beam edge
High BLER, poor SINR and repeated setup failures
VoLTE continuity unreliable across large portions of orbit
Confirms geometry-limited sector-edge weakness

## Slide 8: Serial 2.2 – 1,500 ft
Aircraft simultaneously sees many terrestrial eNodeBs
Very high PCI visibility and mobility activity
Band 40 strongest within beam centre
Outer arcs show repeated setup failures and sparse MOS
Bands 3/20 provide limited supplemental coverage near land

## Slide 9: Serial 2.3 – 3,000 ft
Band 40 dominant serving layer (~90%)
Best RF behaviour within 10–30 km
RF quality degrades progressively toward 50 km and beam edges
10 km arc shows most usable operational behaviour
VoLTE robustness still inconsistent at larger distances

## Slide 10: Serial 2.4 – 6,500 ft
Performance sits between 3,000 ft and 10,000 ft cases
Band 40 sustains inner arcs but deteriorates at 50 km
Limited terrestrial support at this altitude
Predominantly poor MOS despite acceptable RF in beam centre
Strong evidence of geometry-driven service limitations

## Slide 11: Mobility Assessment
Mobility environment highly complex due to large airborne radio horizon
Aircraft UE detects many B3/B20 eNodeBs simultaneously
High intra-LTE handover activity indicates unstable serving-eNodeB dominance
PCI-to-same-PCI events may represent RRC reconfiguration or failed HO attempts
Inter-frequency mobility conclusions require dedicated evidence  IMPROVE PLOTS

## Slide 12: Key Technical Conclusions
Coverage limitations are fundamentally geometry-driven
Wide-beam antenna extends airborne coverage but edge quality remains unstable
Sea reflections and multipath strongly affect RSRQ/SINR
Removing the 12 dB loss would improve results but not eliminate instability
Findings are consistent with Test Case 1 passive measurements

## Slide 13: Recommendations
Evaluate ~5° anticlockwise azimuth optimisation
Investigate small tilt optimisation for edge SINR improvement
Review neighbour relations and airborne mobility tuning
Repeat selected flights with reduced insertion loss
Focus optimisation on wb ant beam edges and 30–50 km offshore regions

## Slide 14: Recommendations
INTRA-LTE HO TBD
5. Interpretation of PCI to same PCI intra-LTE handovers
The Intra-LTE handover figures show a high number of PCI to same PCI intra-LTE handovers, likely to be RRC connection reconfiguration without actual eNodeB change, or a handover failure which is triggered and partially executed but then fails with UE falling back to the original PCI.
There are also few instances where serving PCI changes can be observed without corresponding intra-LTE handover events on the plots. This may be because XCAP may be using different definitions for serving cell change (RF driven) versus handover event (protocol driven), or because these are inter-LTE handover evens that are not captured by the intra-LTE HO plots.